## Slide 1: creosTM syntoprotect

## Slide 2
creos™ biomaterials
a comprehensive portfolio
for soft tissue & bone regeneration
Bone Graft Substitutes
creos™ xenogain
Membranes
creos™ xenoprotect
creos™ syntoprotect
2
Matrix
creos™ mucogain
Notes: US version

## Slide 3
3
creosTM syntoprotect
Your easy choice of dense PTFE membranes to expand grafting options

## Slide 4
creosTM syntoprotect
PTFE membranes
creosTM syntoprotect product range
comprises two product types
Ideal dental membrane for socket grafting and grafting where primary closure is not possible
creosTM syntoprotect
Ti-reinforced PTFE membranes
Ideal membrane for ridge augmentation and grafting bony defects missing one or more wall

## Slide 5
PTFE is a synthetic polymer that is non-resorbable, biologically inert and chemically non-reactive, and therefore an ideal material for many medical device applications.
Colloquially, PTFE-based materials are often referred to by the trade name Teflon from DuPont
In addition to its long history in the field of guided bone regeneration (GBR), PTFE has been used for over 30 years in cardiovascular applications such as suture, vascular grafts and heart valves.
What is PTFE*?
(the material from which creos syntoprotect is made)
*polytetrafluoroethylene

## Slide 6
How does creosTM syntoprotect fit into our barrier membrane portfolio?
For indications between open extraction socket grafting and ridge augmentations we recommend creosTM xenoprotect (resorbable membrane) as barrier membrane.
GBR spectrum
closed technique
Fenestrations/Dehiscences
Small to large defects not requiring structural support
Sinus lifts
creos xenoprotect
Extraction sockets
Extraction sockets
open
technique
creosTM syntoprotect
PTFE membrane
Large defects requiring structural support
(e.g. ridge augmentations)
creosTM syntoprotect
Ti-reinforced PTFE membrane
Notes: IFU

## Slide 7
creosTM syntoprotect product family comprises two product types
The following slides will highlight the application and benefits of the non-reinforced version
creosTM syntoprotect
PTFE membranes
Ideal dental membrane for socket grafting and grafting where primary closure is not possible

## Slide 8
Designed specifically for extraction site grafting and augmentation procedures where exposure to the oral cavity is common
creosTM syntoprotect PTFE membranes

## Slide 9
T=0, Tooth Removed
How is the creosTM syntoprotect PTFE membrane used for extraction socket grafting?

## Slide 10
T=0, bone graft placed

## Slide 11
T=0, bone graft placed

## Slide 12
T=0, creos syntoprotect and non-resorbable sutures placed
The membrane should be trimmed to remain at least 1 mm from adjacent, uninvolved teeth.
The membrane should be trimmed to extend 3-4 mm beyond the defect margins to provide adequate
protection of the bone defect and enhance membrane stability.

## Slide 13
T= 2 weeks post-op, suture removal
For
best results when using textured material, place dimples side up towards gingival tissue.
After trimming, there should be no sharp corners or rough edges.

## Slide 14
T= 2 weeks post-op, suture removal

## Slide 15
T= 4 weeks post-op, membrane removal
The membrane is not intended to remain in place as a permanent implant and should therefore be removed following
the bone regeneration procedure.

## Slide 16
T= 4 weeks post-op, membrane removal
When removal is desired, the
membrane may be easily removed, if exposed, by grasping with forceps and gently removing it from the tissue.

## Slide 17
T= 5 weeks post-op, soft tissue granulating over osteoid

## Slide 18
T= 6-7 weeks post-op, soft tissue completely healed over osteoid

## Slide 19
1. Purposely leave the membrane exposed
      Preservation of the soft tissue architecture and keratinized mucosa
2. 100% dense (non-expanded) PTFE
      Impervious to bacteria (pore size less than 0.3 µm)
3. Soft tissue attaches, but doesn’t grow through the membrane
      Exposed membrane allows for non-surgical removal; no anesthesia required
Why creosTM syntoprotect PTFE membrane?
19

## Slide 20
1. Purposely leave the membrane exposed
20
      Preservation of the soft tissue architecture and keratinized mucosa
The primary advantage of dense PTFE is the ability to remain exposed in the mouth while protecting the underlying defect and bone graft.
Soft tissue architecture is maintained (can be left in its native position), including the interdental papilla and the full width of keratinized mucosa.
A second surgery is not required for membrane removal. Membrane removal is accomplished by grasping the exposed membrane with forceps and gently lifting it from the wound.
© 2008 Osteogenics Biomedical, Inc. BBFY0607
T=0
Preserved mucogingival line
T=3 weeks

## Slide 21
2. 100% dense (non-expanded) PTFE
21
      Impervious to bacteria (pore size less than 0.3 µm)
PTFE as a biomaterial differs in porosity based on the amount of expansion applied during manufacturing.
Dense PTFE is manufactured to eliminate expansion of the nodes and fibrils, resulting in a micro-porous material that is impervious to bacteria while still allowing diffusion of gases and small molecules. the diameter of pathogenic bacteria generally less than 10 μm.
Dense PTFE
creosTM syntoprotect
50 µm
Pore size < 0.3 microns
Expanded PTFE
First Generation PTFE (e.g. GoreTex®)
50 µm
Pore size 30-100 microns
Notes: PTFE is bioinert and does not cause inflammation.
The membrane is soft, flexible and easy to handle.

## Slide 22
3. Soft tissue attaches, but doesn’t grow through the membrane
22
      Exposed membrane allows for non-surgical removal; no anesthesia required
Hexagonal surface dimples (like on a golf ball) provide a textured surface that increases the area available for cellular attachment without increasing porosity.
The increased stability in the wound results in less flap retraction and reduces the risk of membrane movement and loosening.
Removal of dense PTFE is simplified due to the lack of tissue ingrowth into the surface structure.
500 µm
Surface dimples
Cross-section of surface dimple
100 µm
SEM Image courtesy of Schupbach Ltd

## Slide 23
Clinical evidence
Over 30 clinical publications available
1. Barboza EP et al. Implant Dent. 2010;19:2-7.
2. Hoffman O et al. J Periodontol 2008;79:1355-1369.
3. Fotek PD, Neiva RF, Wang HL J Periodontol 2009;80:776-785.
4. Barboza EP, Francisco BS, Ferreira VF. Annual Meeting of the American Academy of Periodontology (AAP) in Seattle, WA, September 6-9, 2008.
23
1. Predictability
In two separate studies treating a total of 696 extraction sites using dense PTFE membranes in an exposed technique, there were no reported infections.1, 2
2. Efficacy
Minimal ridge alterations are observed.3
(1 year post extraction)
Vertical bone loss measured at crest. Horizontal measured from stent to buccal plate.
Non-expanded PTFE membrane utilized over extraction sockets, without primary closure, can be predictably used to promote soft tissue enhancement.4
(90 days post extraction)
Measured as reduction of the occlusal distance between buccal and lingual gingival margins

## Slide 24
Selected open access case series
24
Extraction and Ridge Preservation Followed by Delayed Implant Placement of a Second Mandibular Molar with Proximity to the Inferior Alveolar Nerve
Link to the case series

## Slide 25
Article list

## Slide 26
creosTM syntoprotect product family comprises two product lines
The following slides will highlight the application and benefits of the Titanium-reinforced version
creosTM syntoprotect
Ti-reinforced PTFE membranes
Ideal membrane for ridge augmentation and grafting bony defects missing one or more wall

## Slide 27
The titanium framework provides additional stiffness in the center portion of the membrane while allowing the edges to remain soft and supple. This feature greatly increases membrane rigidity to aid in spacemaking for the repair of larger defects and defects missing adequate bony architecture.
CONFIDENTIAL – INTERNAL USE ONLY
creosTM syntoprotect Ti-reinforced PTFE membranes

## Slide 28
T=0, large defect in mandible
How is the creosTM syntoprotect Ti-reinforced PTFE membrane used for grafting of large bony defects?

## Slide 29
T=0, Defect uncovered with crestal and vertical incisions:
Host bone has been de-corticated
The membrane should be trimmed
to remain at least 1 mm from adjacent, uninvolved teeth.
Adequate flap release must be accomplished in order to achieve a tension-free closure if primary closure is desired.

## Slide 30
T=0, mixture of xenogenic bone graft and autologous bone placed under syntoprotect Ti-reinforced membrane
Membrane fixed with fixation screws.
Dual layer closure achieved PTFE Suture
For best results with textured material, place dimples side up towards gingival tissue.
The use of a
non-resorbable monofilament suture is recommended by the manufacturer.
A double layer closure, with a deep
layer of horizontal mattress sutures followed by a standard wound closure with interrupted sutures, is recommended

## Slide 31
T=2-3 months, Sutures were removed at 14 days, incision line is healing and graft material is consolidating
The membrane may be stabilized with sutures, surgical tacks or screws.

## Slide 32
T= 6-9 months, Graft almost completely consolidated, few residual graft particles still visible. Incision line still slightly everted, but completely healed.
The membrane is not intended to remain in place as a permanent implant and should therefore be removed following
the bone regeneration procedure.

## Slide 33
1. Delicate, lightweight framework
      Easy to trim and compliant with the overlying soft tissues
2. Less is more
      Less titanium bulk allows for greater versatility in shaping and placement, providing additional stability in large, non-spacemaking osseous defects
3. Traditional frame design
      Incorporating delicate and strategically placed titanium “struts” with more than 25 years of clinical history and successful use in GBR
4. Handling options
      Broad portfolio with 13 shapes in 2 thicknesses
Why creosTM syntoprotect Ti-reinforced PTFE membrane?
33

## Slide 34
1. Delicate, lightweight framework
Property of Nobel Biocare
34
Easy to trim and compliant with the overlying soft tissues
The material, including the titanium strut, may be easily cut with surgical scissors. However, with 13 different membrane configurations, aggressive trimming of the membrane is not necessary.

## Slide 35
2. Less is more
Property of Nobel Biocare
35
Less titanium bulk allows for greater versatility in shaping and placement, providing additional stability in large, non-spacemaking osseous defects
The titanium framework is a grade of titanium that has little to no memory. Once formed, the titanium-reinforced membrane will remain in that shape until mechanically altered.
CONFIDENTIAL – INTERNAL USE ONLY
Dense PTFE
Titanium
Dense PTFE
Titanium
cross-section
cross-section
SEM Image courtesy of Schupbach Ltd

## Slide 36
3. Handling options
36
Broad portfolio with 13 shapes in 2 thicknesses
Versatile rectangular shapes These configurations can be trimmed to fit a variety of defects
e.g. shape 4
All available with a thickness of 150 microns and 250 microns
Shapes with fixation points These configurations are designed with fixation points outside of the defect area
e.g. shape 5
e.g. shape 2
Interproximal shapes These configurations are designed to fit between existing teeth

## Slide 37
Clinical evidence
37
Traditional frame design
Incorporating delicate and strategically-placed titanium “struts” with more than 25 years of clinical history and successful use in GBR
More than 20 clinical publications
Easier removal than with more porous titanium mesh and e-PTFE membranes
d-PTFE and e-PTFE membranes showed identical clinical results in the treatment of vertical bone defects around implants, using the GBR technique.5
5. Ronda M, Rebaudi A, Torelli L, Stacchi C. Clin. Oral Impl. Res. 2014 Jul;25(7):859-66.

## Slide 38
Selected open access case series
38
50 µm
50 µm
Ridge preservation/restoration using d-PTFE membranes
Link to the case series
Management of the exposure of a dense PTFE (d-PTFE) membrane in guided bone regeneration (GBR): A case report
Link to the case series

## Slide 39
Article list

## Slide 41
GMT73441 © Nobel Biocare Services AG, 2021 All rights reserved.
Disclaimer: Nobel Biocare, the Nobel Biocare logotype and all other trademarks are, if nothing else is stated or is evident from the context in a certain case, trademarks of Nobel Biocare. Please refer to nobelbiocare.com/trademarks for more information.
Product images are not necessarily to scale. All product images are for illustration purposes only and may not be an exact representation of the product.
Please contact the local Nobel Biocare sales office for current product assortment and availability. Disclaimer: For prescription use only. Caution: Federal (United States) law or the law in your jurisdiction may restrict this device to sale by or on the order of a dentist or a physician. See Instructions For Use for full prescribing information, including indications, contraindications, warnings and precautions
Cytoplast™ (Osteogenics Biomedical, Inc.) is distributed as creos™ syntoprotect since January 2021. Legal Manufacturer: Osteogenics Biomedical, Inc., 4620 71st Street, Bldg 78-79, Lubbock, TX 79424, USA and distributed by Nobel Biocare Services AG.